## Slide 1
Complete MFA Data Pack
Sudostoberbayern Wood Supply Chain
Jon Gurakuqi & Abdul Rehman Mushtaq | TH Rosenheim

## Slide 2
1. Forest Area by Landkreis
JON
Landkreis | Forest (ha) | Bewaldungsgrad | Source
Traunstein | ~56,800 | 37% | AELF Traunstein
Berchtesgadener Land | ~40,200 | 49% | AELF Traunstein
TS + BGL combined | 97,046 | - | AELF Traunstein
Rosenheim (Stadt + Land) | ~48,000 | 33% | AELF Rosenheim
Muhldorf am Inn | 17,500 | 22% | AELF Toging
Altotting | 16,100 | 28% | AELF Toging
MU + AO combined | 33,700 | - | AELF Toging
SOB TOTAL | ~178,700 | ~33% | Computed

## Slide 3
2. Tree Species (SOB / BWI-3 Wuchsgebiete)
JON
Species | Alpenvorland (WG 81) | Alpen (WG 82) | Bayern avg.
Fichte (spruce) | 64.5% | 66.3% | 38.8%
Buche (beech) | 9.6% | 16.8% | 15.3%
Kiefer (pine) | 4.5% | 1.0% | 16.8%
Tanne (fir) | 3.9% | 8.9% | -
Eiche (oak) | 1.5% | - | 7%
Larche (larch) | 0.6% | 0.9% | -
Douglasie | 0.3% | - | -
Other broadleaf | 15.0% | 6.1% | -
Key insight: SOB is much more Fichte-heavy (64-66%) than Bayern average (39%). Higher bark beetle vulnerability.

## Slide 4
3. Forest Ownership
JON
Region | Staatswald | Privatwald | Korperschaftswald
TS + BGL (alpine south) | 57% | 41% | 2%
Muhldorf | 13% | 86% | -
Altotting | 32% | 67% | -
Bayern average | 29.8% | 55.7% | 12.5%
Key insight: Alpine south is state-dominated (easier data access). Northern flatlands are private-dominated (18,000+ owners in TS+BGL alone).

## Slide 5
4. BaySF Forstbetriebe in SOB
JON
Forstbetrieb | Area | Annual cut | Notes
Berchtesgaden | 22,540 ha HB | 103,400 Fm/yr plan 92,740 Fm actual 2022 | Dr. Daniel Muller
Ruhpolding | ~36,000 ha total | Not public | 53% Fichte, 2/3 Schutzwald
Wasserburg a. Inn | ~20,000 ha | ~160,000 Fm/yr (8.9 Fm/ha/yr) | Covers MU, AO, parts RO

## Slide 6
5. Harvest & Schadholz (Bayern -> SOB scaling)
JON
Year | Bayern Total (Mio Fm) | Schadholz (Mio Fm) | Schadholz % | SOB est. (x6.9%)
2020 | 18.0 | 10.7 | ~60% | 1.24
2021 | 18.95 | 6.2 | 33% | 1.31
2022 | 20.89 | ~7.1 | 34% | 1.44
2023 | 22.18 | 11.3 | 51% | 1.53
2024 | 20.65 | 10.7 | 52% | 1.42
Sortiment split 2024: Stammholz 51% | Energieholz 37% | Industrieholz 7% | Not used 5%
Source: LWF Bayern Holzeinschlagserhebung

## Slide 7
6. Construction Demand & Holzbauquote
JON
Year | Bayern Baugenehmigungen | YoY change | Holzbauquote
2022 | 65,200 | - | ~26%
2023 | 58,732 | -12% | ~26.5%
2024 | 51,513 | -12.3% | 27%
2025 | 54,149 | +5.1% | ~27%
Q1 2026 | 15,325 | +12.1% | -
Holzbauquote trend: 19.5% (2013) -> 22% (2020) -> 27% (2024)
Wood per EFH: 15-25 m3 sawn timber | MFH/Hybrid: 30-60 m3
Landwirtschaftliche Gebaude: 47% Holzbauquote
Dominant material overall: Ziegel 55%, Holz 27%, Porenbeton 10%
Source: Bayerisches Landesamt fur Statistik, LWF Bayern, Holzbau Deutschland

## Slide 8
7. SOB Sawmill Structure
ABDUL
Variable | Value | Source
SOB sawmills | 77 | Verein Wir bauen auf heim. Holz
Size class | Mostly small/medium | LWF/Mantau
No industrial Grosssagewerk | Since Aicher 1979 | Regional history
Bayern conversion yield | 59% | LWF/CARMEN 2022
SOB est. roundwood input | 800,000-1,300,000 Fm/yr | Estimated
SOB est. sawn timber out | 480,000-800,000 m3/yr | Estimated
SOB est. by-products | 300,000-500,000 m3/yr | Estimated
Energy cost share | 2.4% of GPV | Destatis
Key issue: No large sawmill in SOB -> roundwood exported to Austrian mills (Pfeifer, Binderholz, Hasslacher) then sawn timber re-imported.

## Slide 9
8. Imports & Exports (Bayern level)
ABDUL
Flow | Volume 2024 | Partners
Roundwood export -> AT | 2.0 Mio Fm (+20%) | AT = 78% of Bayern softwood export
Schnittholz export | 2.8 Mio m3 (-7%) | USA 21%, AT 18%, IT 8%, CN 8%
Schnittholz import | 0.8 Mio m3 (+22%) | AT 32%, CZ 14%
Nadelrundholz -> AT | 1.8 Mio Fm | AT 78%, rest AT 90% Buche
Eichenrundholz export | - | BE 61%, CN 21%
SOB is disproportionately affected: BGL borders Salzburg, TS borders Salzburg + Tirol, AO borders Oberosterreich. SOB roundwood physically flows to Austrian mills.
Source: LWF Bayern Aussenhandel 2024

## Slide 10
9. Zimmerer / Timber Construction Demand
ABDUL
Innung | Meisterhaft Betriebe | Landkreise
Zimmerer-Innung TS/BGL | 30 | Traunstein, BGL
Zimmerer-Innung Rosenheim | 51 | RO Stadt + Land
Zimmerer-Innung MU/AO | 18 (2019) | Muhldorf, Altotting
SOB total (Innungs) | ~99 | -
SOB est. total (all) | 200-250 | incl. non-Innung
Estimated SOB Zimmerer demand: 100,000-180,000 m3 sawn timber/yr
(200-250 Betriebe x 500-800 m3 avg per Betrieb)
Key regional initiative: Verein 'Wir bauen auf heimisches Holz e.V.'

## Slide 11
10. Bayern Reference Numbers (BWI 2022)
Variable | Value
Total forest area | 2.617 Mio ha (37.1% bewaldet)
Standing stock | 1.011 Bn Vfm
Mean Hektarvorrat | 405 Vfm/ha (highest in Germany)
Annual increment | 25.7 Mio Vfm/yr (10.4 Vfm/ha/yr)
Active utilization | 22.1 Mio Vfm/yr
Natural mortality | 3.3 Mio Vfm/yr
Totholz | 29.9 m3/ha (+7.9 vs 2012)
Nadelholz/Laubholz (area) | 61.6% / 38.4%
SOB share of Bayern | 6.9% (178,700 / 2,617,000 ha)
Source: LWF Bayern, Bundeswaldinventur 2022